## Slide 1
LOUISIANA TECH
UNIVERSITY
RAW 2026
PhD Forum
AI Workload Acceleration through Semantic Preserving Hardware Generation
Md Mahfuzul Haque • Md Rubel Ahmed
Louisiana Tech University
Methodology: Two RTL Generation Flows
LUT Efficiency
Chart: 
| Increment | ReLU | GELU | GEMM | FFNN
Allo+Calyx | 15 | 50 | 50 | 250 | 500
ChatGPT 5.2 | 50 | 250 | 500 | 3000 | 1200
Gemini 3 Pro | 15 | 250 | 500 | 1200 | 500
Key Findings
1.7×
higher Fmax
vs ChatGPT
75%
fewer LUTs
vs ChatGPT
1.4×
higher Fmax
vs Gemini
50%
fewer LUTs
vs Gemini
Compiler-driven flow consistently outperforms LLM-driven RTL generation across all benchmarks due to explicit scheduling, optimization passes, and semantic-preserving transformations.
Future Directions
Calyx
Reference Model/Algo.
memref
Linalg
Affine
SCF
/
Prompt
Calyx IR
Very high-level Abstraction
.sv
LLMs
Modular verification
Syntax Check
GPT
Gemini
Fail
Simulation on Vivado
QoR Analysis
High-level MLIR
Mid-level MLIR
Low-level MLIR
CIRCT Dialects
Reference Model/Algo.
Allo
torch.fx
Allo-MLIR
Semantic-preserving compilation: Retain high-level dataflow across all lowering stages
Resource-aware DSE framework: Choose tiling, unrolling, pipelining, memory banking, and precision under FPGA constraints.
Push-Button HLS: Generate synthesizable hardware from high-level AI workload specifications.
LLMs as assistants: Use LLMs for front-end assistance, pragma suggestions, debugging, and design-space hints
Research Problem & Motivation
Demand for workload-aware accelerators is skyrocketing, but hand-crafting RTL requires extreme microarchitectural expertise
LLMs can generate RTL from high-level descriptions, but their probabilistic token prediction lacks explicit execution models, leading to conservative, unoptimized pipelines.
Conventional compilers strip high-level loop and dataflow structures during sequential lowering, weakening spatial mapping capabilities.
Central Research Question:
How can a hardware compiler preserve the high-level semantic structure of AI workloads while progressively lowering them into efficient, resource-aware spatial implementations for reconfigurable heterogeneous SoCs?
Key Challenges in Push-Button Design
Resource utilization, clock frequencies, and critical timing paths are only accurately known after full downstream vendor synthesis.
Compiler must decide tiling, pipelining, unrolling, memory partitioning, and dataflow mapping without manual expert tuning.
Performance Comparison – Fmax (MHz)
Chart: 
| Increment | ReLU | GELU | GEMM | FFNN
Allo+Calyx | 450 | 380 | 320 | 280 | 200
ChatGPT 5.2 | 265 | 224 | 188 | 165 | 118
Gemini 3 Pro | 321 | 271 | 229 | 200 | 143
For further details: